## Slide 1: Considerations in the Design of Wearable Robotics for Distal Upper Extremity
Avinash Baskaran
Chad G. Rose

## Slide 2: Distal Upper Extremity

## Slide 3: Neuromuscular patterns are governed by the central nervous system
Motor Control region of the Frontal Lobe:
Motor neuron generates potential
(thought to be a DC PWM signal)
Signal pathway:
Analog voltages transmitted through a synaptic cascade
Nervous junction
Signal distribution
Neuromuscular junction:
Signal delivered to muscle fibers
Muscle excitation
https://www.sciencedirect.com/science/article/pii/S0960982206018252

## Slide 4: Non-invasive sensors can be used to characterize neuromuscular patterns
Kinematic Sensing
Signal Analysis and processing
Non-invasive Myographic Sensing
Recognition of
Muscle Activation and Recruitment

## Slide 5: Neuromuscular patterns can inform human-robot interaction
Kinematic Sensing
Signal Analysis and processing
Non-invasive Myographic Sensing
Recognition of
Muscle Activation and Recruitment
Assistance

## Slide 6: Neuromuscular pattern analysis can be used to predict and minimize fatigue
Decreased Motor Neuron Firing due to electrochemical diffusion into and from adjacent brain regions and neurons
Accumulation of Central Fatigue Reduced capacity of central nervous system to voluntarily activate motor units
Neuromuscular Junction:
Acetylcholine depletion due to increased muscle innervation, action potential frequency
Accumulation of peripheral fatigue Weakened Skeletal Muscle contractility due to increased lactate concentration (byproduct of ATP metabolism), decreased pH, diminished potential for electrolytic response
Notes: The point: Neuromuscular Fatigue is both central and peripheral to the Neuromuscular system and is caused by the degradation of electrochemical gradients

## Slide 7: Neuromuscular fatigue analysis has a wide variety of applications
https://ir.eksobionics.com
https://spectrum.ieee.org
https://www.army-technology.com
https://media.gm.com/

## Slide 8: Focusing on Hand/Upper Extremity Fatigue

## Slide 9: The primary contributions of this research:
Implementing a sensor-fusion spectral analysis method for Robust characterization of neuromuscular patterns
Using this method to identify fatigue and stability from neuromuscular activation data in real time
Proving that the estimates correlate well with real and perceived effects (ie. Fatigue, movement smoothness, etc.)

## Slide 10: Common sEMG sensing for upper limb (1)

## Slide 11: Muscles involved in voluntary movement of the arm
Elbow:
Flexion (143°)
  Biceps brachii
  Brachioradialis
  Brachialis
Extension (5°)
  Triceps
Pronation (78°)
  Pronator teres
  Pronator quadratus
  Flexor carpi radialis
Supination (85°)
  Biceps Brachii
Shoulder:
Shoulder flexion
  Anterior deltoid
  Pectoralis major
  Coracobrachialis
Shoulder extension
  Latissimus dorsi
  Teres major
  Teres minor
  Posterior deltoid
Shoulder abduction
  Supraspinatus
  Deltoid
  Trapezius
  Serratus anterior.
Shoulder adduction
  Pectoralis major
  Latissimus dorsi
  Teres major
  Triceps
  Coracobrachialis
Medial rotation
  Subscapularis
  Teres major
  Pectoralis major
  Latissimus dorsi
Lateral rotation
  Infraspinatus
  Teres minor
Wrist:
Flexion (73°)
  Flexor carpi ulnaris
  Flexor carpi radialis
  Flexor digitorum superficialis
Extension (71°)
  Extensor carpi radialis longus
  Extensor carpi radialis brevis
  Extensor carpi ulnaris
  Extensor digitorum
Radial deviation (19°)
  Flexor carpi radialis
  Extensor carpi radialis longus
  Extensor carpi radialis brevis
Ulnar deviation (33°)
  Flexor carpi ulnaris
  Extensor carpi ulnaris
Fingers:
Flexion
  Flexor digitorum profundus
  Flexor digitorum superficialis
Extension
  Extensor digitorum
  Extensor digitorum minimi
Abduction
  Dorsal interossei
Abduction
  Palmar interosseous muscles

## Slide 12: Unique muscles involved in voluntary movement of the arm
Elbow:
Flexion (143°)
  Biceps brachii
  Brachioradialis
  Brachialis
Extension (5°)
  Triceps
Pronation (78°)
  Pronator teres
  Pronator quadratus
  Flexor carpi radialis
Supination (85°)
  Biceps Brachii
Shoulder:
Shoulder flexion
  Anterior deltoid
  Pectoralis major
  Coracobrachialis
Shoulder extension
  Latissimus dorsi
  Teres major
  Teres minor
  Posterior deltoid
Shoulder abduction
  Supraspinatus
  Deltoid
  Trapezius
  Serratus anterior.
Shoulder adduction
  Pectoralis major
  Latissimus dorsi
  Teres major
  Triceps
  Coracobrachialis
Medial rotation
  Subscapularis
  Teres major
  Pectoralis major
  Latissimus dorsi
Lateral rotation
  Infraspinatus
  Teres minor
Wrist:
Flexion (73°)
  Flexor carpi ulnaris
  Flexor carpi radialis
  Flexor digitorum superficialis
Extension (71°)
  Extensor carpi radialis longus
  Extensor carpi radialis brevis
  Extensor carpi ulnaris
  Extensor digitorum
Radial deviation (19°)
  Flexor carpi radialis
  Extensor carpi radialis longus
  Extensor carpi radialis brevis
Ulnar deviation (33°)
  Flexor carpi ulnaris
  Extensor carpi ulnaris
Fingers:
Flexion
  Flexor digitorum profundus
  Flexor digitorum superficialis
Extension
  Extensor digitorum
  Extensor digitorum minimi
Abduction
  Dorsal interossei
Abduction
  Palmar interosseous muscles
13
7
8
6

## Slide 13: Common sEMG sensing for upper limb: Shoulder
Shoulder Flexion Extension
  da Silva et. al.
    Latissimus dorsi
    Anterior deltoid

## Slide 14: Common sEMG sensing for upper limb: Elbow
Elbow Flexion Extension
  Ghonasgi et. al. Harmony Exoskeleton:
    Biceps brachii
    Triceps brachii
  Madden et. al. monitoring fatigue (“The scope of this paper requires analysis of only the muscles that extend the elbow, that is, the triceps brachii and anconeus”)
    Triceps Brachii
      Long (1), lateral (2), and medial heads (3)
    Anconeus Muscles (4)
    Biceps Brachii
    Brachioradialis
    Deltoid
      Anterior, Middle, and Posterior
  da Silva et. al.
    Biceps brachii
    Triceps

## Slide 15: Common sEMG sensing for hand grasps
Various hand grasps / finger extension patterns
  Y. Yun Maestro
    “several hand grips share similar muscle activity patterns, and surface EMG sensors cannot pick up individual muscle signals…
    three…distinctive hand poses… transverse volar grip, lateral pinch, and extension grip”
    Flexor Digitorum Superficialis
    Extensor digitorum
    Flexor Pollicis Brevis/Abductor Pollicis Brevis
    (taken together; collocated)
Notes: “criteria for… (placement of sEMG electrodes) include” first that the EMG sensor must be able to measure the muscle activity of a muscle group that generates the target hand poses, second that the EMG sensors must measure non-redundant EMG signals compared to other signals measured by other EMG sensors, and lastly that EMG signals must be available for SCI subjects.”

## Slide 16: Common sEMG sensing for upper limb
Elbow Flexion/Extension, Forearm pronation/supination, Wrist flexion/extension, Wrist radial-ulnar deviation
  McDonald et. al. MAHI Exo-II:
    Bicep Brachii ???
    Flexor Carpi radialis???
    Flexor Carpi Ulnaris ???
    Brachioradialis ???

## Slide 17: (ASGC ‘21) Space Applications
Majority of space grasps fall into a well-defined set:
  Power Grasp: five fingers, with the thumb opposing)
  Two-finger (precision) pinch: thumb and index finger
  Three-finger (precision) pinch: thumb opposing index and middle finger
  Lateral (intermediate) pinch: thumb opposing the side of the fist.

## Slide 18: (ASGC ‘21) Space Applications

## Slide 19: Fatigue: Frequency analysis reveals neuromuscular fatigue in isometric contractions
Isometric contraction – constant muscle length
“Amplitude and spectral parameters of the sEMG signal are closely related to the biochemical correlates of muscle fatigue.” [d]
“Decreasing trends in the sEMG median frequency [7], a spectral indicator estimated from the power spectral density of the signal, is a classical measure for quantifying and observing muscle-level fatigue” [d]
However such methods not “effective in identifying fatigue during dynamic force contractions” [d]
Notes: sEMG readings of Isometric (ie. Constant force) muscle contraction can be considered wide-sense stationary (WSS) random process (ie. Statistically time invariant cumulative distribution)[d]

## Slide 20: Fatigue: Dynamic contraction EMG profile more complex
Dynamic (isotonic) contraction – non-constant muscle length
Statistical non-stationarity of sEMG spectral patterns during dynamic force contractions makes fatigue analysis more difficult.
“Time-frequency distribution-based spectral estimation has shown to overcome the challenges of sEMG non-stationarity and have been proven effective in identifying fatigue during dynamic force contractions”
Notes: sEMG readings of Isometric (ie. Constant force) muscle contraction can be considered wide-sense stationary (WSS) random process (ie. Statistically time invariant cumulative distribution)[d]

## Slide 21: Fatigue: Estimation by Spectral Analysis
Where:
  is two-dimensional probability density function
  is energy of the sEMG signal
  * is complex conjugate
  is TFD kernel
TFD Kernel:
Sliding window bounds:

## Slide 22: Co-activation stability: synergistic co-activation is effected by fatigue
Muscle Synergy Theory: Some controversy but also some unanimity
“To analyze upper limb synergies, we applied non-negative matrix factorization to 14 EMG signals from muscles of 11 participants performing isometric contractions. A preliminary multidirectional task was used to identify synergy directional tuning.”

## Slide 23: Non-negative matrix factorization (a state variable approach to modeling neuromuscular fatigue)
https://openbioinformaticsjournal.com/VOLUME/11/PAGE/53/FULLTEXT/
https://journals.plos.org/ploscompbiol/article?id=10.1371/journal.pcbi.1004737
https://www.nature.com/articles/s41598-020-65257-w
General form:
Iterative implementation

## Slide 24: Bibliography
[a] https://journal.stemfellowship.org/doi/pdf/10.17975/sfj-2017-011
[b] https://pubmed.ncbi.nlm.nih.gov/15698666/
[c] https://citeseerx.ist.psu.edu/viewdoc/download?doi=10.1.1.403.1405&rep=rep1&type=pdf
[d] https://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=8396816
[e] https://pubmed.ncbi.nlm.nih.gov/29537913/
[f] file:///C:/Users/azb0180/Downloads/Fatigue_Influences_the_Recruitment_but_Not_Structu.pdf
[g] https://www.researchgate.net/publication/338586297_Estimating_the_Effect_of_Robotic_Intervention_on_Elbow_Joint_Motion/figures?lo=1
[h] https://mahilab.rice.edu/sites/default/files/page-files/2017_ICRA_Yun.pdf