## Slide 1
                Toward the Future of Manned Space Exploration:
                A Novel Wearable Interface for Optimal Human-Robot Collaboration
                Avinash Baskaran and Dr. Chad G. Rose
                Department of Mechanical Engineering, Auburn University
Modeling fatigue: For non-isometric tasks, changes in sEMG time-frequency spectral characteristics correlate to muscular fatigue
Estimating intent: Decomposition of sEMG signal matrices provides contributions of muscles (W[i,j]) to intended movements, (H[i,j]).
Fatigue Estimation Process
Intent Prediction Process
BACKGROUND
Funded by: NASA Space Grant College and Fellowship Program
(left: Astronaut Sunita Williams using a high torque hand-held tool, right: A robotic hand device for assistance during space walks)
Human-Robot interaction (HRI) can help astronauts during dangerous or taxing EVAs by providing assistive forces and torques to reduce neuromuscular load
Sub-optimal interaction between humans and robots produces antagonistic forces and torques, diminishing control stability and degrading performance
[1] S. Boyas and A. Gu evel. Neuromuscular fatigue in healthy muscle: Underlying factors and adaptation mechanisms. Annals of Phys. and Rehab. Med., 2011.
[2] O. Celik, M. O’Malley, C. Boake, H. Levin, N. Yozbatiran, and T. Reistetter. Normalized movement quality measures for therapeutic robots strongly correlate with clinical motor impairment measures. IEEE Trans. on Neural Systems and Rehab. Engineering, 2010.
[4] M. L. Gernhardt, J. A. Jones, R. A. Scheuring, A. F. Abercromby, J. A. Tuxhorn, and J. R. Norcross. Risk of compromised eva performance and crew health due to inadequate eva suit systems. 2009.
[5] E. Jovanov, I. K. Small, T. D. Rolin, H. Ganegoda, and C. Hill. Long term monitoring of respiration and co2 using flexible printed sensors. 2020.
Human
Robot
Wearable interface
SIGNALS
SIGNALS
FORCES
3D printed flexible surface electrodes embedded in a wearable device allow for analysis of neuromuscular characteristics including fatigue and movement intent.
The target muscles are: Flexor digitorum superficialis (left), extensor digitorum (middle), flexor pollicis brevis (right)
REFERENCES
[6] K. E. Madden, A. Deshpande, B. J. Peters, J. M. Rogers, E. A. Laske, and E. McBryan. The influence of robotic assistance on reducing neuromuscular effort and fatigue during extravehicular activity glove use. 2017.
[7] J. Massion, V. Gurfinkel, M. Lipshits, A. Obadia, and K. Popov. [strategy and synergy: two levels of equilibrium control during movement. effects of the microgravity].Comptes rendus de l’Academie des sciences. Serie III, Sciences de la vie, 1992.
[8] K. Min, D. Shin, J. Lee, and S. Kakei. Electromyogram refinement using muscle synergy based regulation of uncertain information. Journal of biomechanics, 2018.
[9] S. A. Overduin, A. d’Avella, J. Roh, and E. Bizzi. Modulation of muscle synergy recruitment in primate grasping. J. of Neuroscience, 2008.
[10] J. Rogers, B. Peters, E. Laske, and E. McBryan. Development and testing of robotically assisted extravehicular activity gloves. 47th International Conference on Environmental Systems, 2017.
[11] C. G. Rose and M. O’Malley. Hybrid rigid-soft hand exoskeleton to assist functional dexterity. IEEE Rbtcs. and Automtn. Letters, 2019.
[12] S. A. Safavynia, G. Torres-Oviedo, and L. Ting. Muscle synergies: Implications for clinical evaluation and rehabilitation of movement. Topics in spinal cord injury rehabilitation, 2011.
Preliminary results suggest that the interface is able to model both neuromuscular fatigue and movement intent accurately, advancing the state of the art in HRI
This work meets a need in the literature, as no other work has presented such an approach. It also meets practical needs in Space-suit mounted robotics and human robot interaction more broadly. Future work will include a comprehensive system usability study
Experimental Validation Protocol
Stage 1. Validation
Stage 3. Trial with spacesuit conditions
Original sEMG signal (5 sec)
Hand activity
Fatigue detected
TFD Signal energy
Stage 2. Comprehensive human subjects trial
METHODS
(current stage)
CONCLUSIONS
IMPLEMENTATION
Pose detected
3D printed
Flexible sensor electronics