## Slide 1
                TOWARD THE FUTURE OF MANNED SPACE EXPLORATION
                A NOVEL WEARABLE INTERFACE FOR OPTIMAL HUMAN-ROBOT COLLABORATION
                Avinash Baskaran and Chad G. Rose
                Department of Mechanical Engineering, Auburn University
Modeling fatigue: For non-isometric tasks, sEMG time-frequency spectral characteristics correlate to fatigue
Estimating intent: Decomposition of sEMG signal gives muscles contributions (W[i,j]) to intended movements, (H[i,j]).
Fatigue Estimation Process
Intent Prediction Process
Funded by: NASA Space Grant Consortium
(left: Astronaut Sunita Williams using a high torque hand-held tool, right: A robotic hand device for assistance during space walks)
Human-Robot interaction (HRI) can help astronauts during dangerous or taxing EVAs by providing assistive forces and torques to reduce neuromuscular load
Sub-optimal interaction between humans and robots produces antagonistic forces and torques, diminishing control stability and degrading performance
[1] S. Boyas and A. Gu evel. Neuromuscular fatigue in healthy muscle: Underlying factors and adaptation mechanisms. Annals of Phys. and Rehab. Med., 2011.
[2] O. Celik, M. O’Malley, C. Boake, H. Levin, N. Yozbatiran, and T. Reistetter. Normalized movement quality measures for therapeutic robots strongly correlate with clinical motor impairment measures. IEEE Trans. on Neural Systems and Rehab. Engineering, 2010.
[4] M. L. Gernhardt, J. A. Jones, R. A. Scheuring, A. F. Abercromby, J. A. Tuxhorn, and J. R. Norcross. Risk of compromised eva performance and crew health due to inadequate eva suit systems. 2009.
[5] E. Jovanov, I. K. Small, T. D. Rolin, H. Ganegoda, and C. Hill. Long term monitoring of respiration and CO2 using flexible printed sensors. 2020.
3D printed flexible electrodes embedded in a fabric sleeve will be used to estimate fatigue and movement intent for more optimal human-robot collaboration
target muscles: Flexor digitorum superficialis (top), extensor digitorum (middle), flexor pollicis brevis (bottom)
[6] K. E. Madden, A. Deshpande, B. J. Peters, J. M. Rogers, E. A. Laske, and E. McBryan. The influence of robotic assistance on reducing neuromuscular effort and fatigue during extravehicular activity glove use. 2017.
[7] J. Massion, V. Gurfinkel, M. Lipshits, A. Obadia, and K. Popov. [strategy and synergy: two levels of equilibrium control during movement. effects of the microgravity].Comptes rendus de l’Academie des sciences. Serie III, Sciences de la vie, 1992.
[8] K. Min, D. Shin, J. Lee, and S. Kakei. Electromyogram refinement using muscle synergy based regulation of uncertain information. Journal of biomechanics, 2018.
[9] S. A. Overduin, A. d’Avella, J. Roh, and E. Bizzi. Modulation of muscle synergy recruitment in primate grasping. J. of Neuroscience, 2008.
[10] J. Rogers, B. Peters, E. Laske, and E. McBryan. Development and testing of robotically assisted extravehicular activity gloves. 47th International Conference on Environmental Systems, 2017.
[11] C. G. Rose and M. O’Malley. Hybrid rigid-soft hand exoskeleton to assist functional dexterity. IEEE Rbtcs. and Automtn. Letters, 2019.
[12] S. A. Safavynia, G. Torres-Oviedo, and L. Ting. Muscle synergies: Implications for clinical evaluation and rehabilitation of movement. Topics in spinal cord injury rehabilitation, 2011.
Preliminary results suggest that the interface is able to model both neuromuscular fatigue and movement intent accurately, advancing the state of the art in HRI
Experimental Validation Protocol
Stage 1. Validation
Stage 3. Trial w/ spacesuit glove
Fatigue detected
Stage 2. Comprehensive human subjects trial
Pose detected
BACKGROUND
METHODS
REFERENCES
This work meets practical needs in space-suit mounted robotics and human robot interaction more broadly, as no other work has presented such an approach. Future work will include a comprehensive system usability study
IMPLEMENTATION
CONCLUSIONS
3D printed
Flexible sensor electronics
Human
FORCES
Robot
Wearable interface
SIGNALS
SIGNALS
Classifier identifies hand pose
And correlates fatigue with pose to direct robot
To validate the method, an sEMG signal was processed via the intent prediction and fatigue estimation process
Hand pose
Intent & fatigue modeling
Robotic assistance

## Slide 2
Raw sEMG measurements
Joint time-frequency distribution
Filter (10-400 Hz)
Fatigue estimation
Probability density of sEMG signal amplitude, ai(t), is analyzed in conjunction with instantaneous frequency, fin(t), to model and predict “neural drive”, a correlate of fatigue that can be modeled
Non-negative Matrix Factorization
Intent estimation
Decomposition of matrix composed of multiple sEMG signals produces data vectors describing of individual muscle contributions (W[i,j]) to synergistic coactivation patterns (H[i,j])
Human-robot interaction plays a key role in healthcare, automation, and military infrastructure, and will continue to enhance human performance in these and other areas.
No standard interface has yet been developed to evaluate and predict muscle fatigue and movement intent.
Human
Robot
Sleeve-like wearable sEMG Interface
SIGNALS
SIGNALS
FORCES

## Slide 7
                Toward the Future of Manned Space Exploration:
                A Novel Wearable Interface for Optimal Human-Robot Collaboration
                Avinash Baskaran and Dr. Chad G. Rose
                Department of Mechanical Engineering, Auburn University
Processing of the muscle signals includes joint analysis of the probability density of sEMG signal amplitude, ai(t), and instantaneous frequency, fin(t) to model and predict fatigue. Decomposition of sEMG signal matrices will quantify contributions of muscles (W[i,j]) to intended movements models (H[i,j]).
Joint time-frequency distribution
Non-negative Matrix Factorization
Intent estimation
BACKGROUND
This work presents a novel human-robot interface which analyzes user fatigue and movement intent using surface electromyography.
reduces garment, It generates and communicates control parameters to wearable robots to minimize their response latency and minimize user fatigue. No other work has presented such an approach, and this work meets a need not only in the literature, but also a felt need in areas such as tele-health and rehabilitation, to Space-suit mounted robotic assistance. Future work includes a comprehensive system usability and efficacy study in a human-subjects context.
Funded by: NASA Space Grant College and Fellowship Program
(left: Astronaut Sunita Williams using a high torque hand-held tool, right: A robotic hand device for assistance during space walks)
Robots can assist astronaut during dangerous or taxing EVAs by providing assistive forces and torques to reduce neuromuscular load.
Sub-optimal interaction between humans and robots due to produces antagonistic forces and torques, diminishing control stability and degrading performance
[1] S. Boyas and A. Gu evel. Neuromuscular fatigue in healthy muscle: Underlying factors and adaptation mechanisms. Annals of Phys. and Rehab. Med., 2011.
[2] O. Celik, M. O’Malley, C. Boake, H. Levin, N. Yozbatiran, and T. Reistetter. Normalized movement quality measures for therapeutic robots strongly correlate with clinical motor impairment measures. IEEE Trans. on Neural Systems and Rehab. Engineering, 2010.
[4] M. L. Gernhardt, J. A. Jones, R. A. Scheuring, A. F. Abercromby, J. A. Tuxhorn, and J. R. Norcross. Risk of compromised eva performance and crew health due to inadequate eva suit systems. 2009.
[5] E. Jovanov, I. K. Small, T. D. Rolin, H. Ganegoda, and C. Hill. Long term monitoring of respiration and co2 using flexible printed sensors. 2020.
Human
Robot
Sleeve-like wearable interface
SIGNALS
SIGNALS
FORCES
A wearable interface embedded with surface electrodes allow for analysis of neuromuscular characteristics including fatigue and intent
Flexor digitorum superficialis (left), extensor digitorum (middle), flexor pollicis brevis (right)
Fatigue estimation
METHODS
REFERENCES
[6] K. E. Madden, A. Deshpande, B. J. Peters, J. M. Rogers, E. A. Laske, and E. McBryan. The influence of robotic assistance on reducing neuromuscular effort and fatigue during extravehicular activity glove use. 2017.
[7] J. Massion, V. Gurfinkel, M. Lipshits, A. Obadia, and K. Popov. [strategy and synergy: two levels of equilibrium control during movement. effects of the microgravity].Comptes rendus de l’Academie des sciences. Serie III, Sciences de la vie, 314 2:87–92, 1992.
[8] K. Min, D. Shin, J. Lee, and S. Kakei. Electromyogram refinement using muscle synergy based regulation of uncertain information. Journal of biomechanics, 72:125–133, 2018.
[9] S. A. Overduin, A. d’Avella, J. Roh, and E. Bizzi. Modulation of muscle synergy recruitment in primate grasping. J. of Neuroscience, 28:880 – 892, 2008.
[10] J. Rogers, B. Peters, E. Laske, and E. McBryan. Development and testing of robotically assisted extravehicular activity gloves. 47th International Conference on Environmental Systems, 2017.
[11] C. G. Rose and M. O’Malley. Hybrid rigid-soft hand exoskeleton to assist functional dexterity. IEEE Robotics and Automation Letters,4:73–80, 2019.
[12] S. A. Safavynia, G. Torres-Oviedo, and L. Ting. Muscle synergies: Implications for clinical evaluation and rehabilitation of movement. Topics in spinal cord injury rehabilitation, 17 1:16–24, 2011.
IMPLEMENTATION
CONCLUSIONS